## Slide 1: 19Z604 Embedded Systems
Dr.N.Arulanand,
Professor,
Dept of CSE,
PSG College of Technology

## Slide 2: Resource Sharing
Resource Sharing among real-time tasks
CPU is a serially reusable resource
  Can be used by one task at a time
  The task can be preempted at any time without affecting correctness
Other resources:
  files, data structures, Memory, devices,
  These resources need to be used in preemptable mode.

## Slide 3: Resource Sharing
Critical Section
A part of the section in while a shared non-preemptable resource is accessed
Traditional solution in Operating System to execute critical section
  Semaphores
In Real-time systems, the solution doesn’t work. It leads to
  Priority Inversion
  Unbounded Priority Inversion

## Slide 4: Priority Inversion
Priority Inversion
  Priority inversion is a situation in which a low-priority task executes while a higher priority task waits on it due to resource contentions
Consequences in Real time system
  If a task cannot be preempted (a low priority task) while computing a critical section
  The higher priority task keeps waiting
  Task Scheduling Algorithm: Low Priority task should yield to Higher priority task (ex: RMA) .
  Basic assumption in Real Time Task Scheduling is Higher Priority will execute first....

## Slide 5: Bounded Priority Inversion

## Slide 6: Unbounded Priority Inversion
A complex problem than bounded priority inversion
  Situation: Low priority task is holding a resource.
  After some time, High priority task executes and waiting for TL to complete
  Intermediate tasks, which doesn’t need to resource preempts to low priority task.

## Slide 7: Unbounded Priority Inversion Example
T1 has highest priority; T6 has lowest priority
T1 Missing deadline....

## Slide 8: Mars PathFinder
4th July 1997, landed on the Mars surface
Bounced on the martian surface, surrounded by airbags
Deployed the Sojourner Rover
Gathered and transmitted enormous data to the earth

## Slide 9: Mars PathFinder – Sojourner Rover

## Slide 10: Pictures from Mars PathFinder

## Slide 11: Mars PathFinder Gitch
Often started Resetting
They were using real-time kernel from Wind River Systems Ltd – VxWorks RTOS
VxWorks can run in Trace mode:
  Events like context switching, use of synchronisation objects and interrupts are recorded
  Replicate the precise condition for reset
  Unbounded priority inversion was occurring
  Found global variable to initialize the Priority Inheritance was turned OFF

## Slide 12: Solution to Priority Inversion
How to make a task complete as early as possible ?
Priority Inheritance Protocol
Priority Ceiling Protocol

## Slide 13: Priority Inheritance Protocol
Raise the priority of Low Priority Task (if it’s holding the resource of higher priority)
The priority is raised to the level of the task that is holding the resource.

## Slide 14: Priority Inheritance Protocol
As soon as the task release its resource,
It gets back to its original priority value if it holding no other critical resource
If in case, its holding other critical resources:
It inherits the priority of the highest priority task waiting for resource.

## Slide 15: Three Tasks and 2 resources

## Slide 16: Priority Inheritance Protocol
PIP resolves unbounded priority inversion issue.
These two issues still persist:
Deadlock
Chain Blocking

## Slide 17: Deadlocks

## Slide 18: Deadlock – Example 2

## Slide 19: Chain Blocking
Each time a Task needs a resource, it needs to undergo priority inversion
Example: A high priority task T1 needs several resources.....from other tasks...

## Slide 20: Chain of Nested Resource Locks

## Slide 21: Priority Ceiling Protocol
Ceiling priority of a resource
As soon as a task acquires a Resource, it’s priority value is raised to the ceiling priority of that resource

## Slide 22: Priority Ceiling Protocol
Solves the problem of unbounded priority inversion, deadlock and chain blocking

## Slide 23: Example
In Unix, lower priority value indicates higher priority
In Windows, lower value indicates lower priority

## Slide 24: Priority Ceiling Protocol
Unbounded priority inversion is resolved

## Slide 25: Priority Ceiling Protocol - Issues
Inheritance Blocking:
  When a priority value of a low priority task holding a resource is raised to higher value
  Intermediate priority tasks not needing the resource, cannot execute and hence undergo priority inversion.....
Practically, it’s not possible to know when a resource is needed by a task...