## Slide 1: 19Z604 Embedded Systems
Dr.N.Arulanand,
Professor,
Dept of CSE,
PSG College of Technology

## Slide 2: Types of Schedulers
1. Clock-driven Schedulers : based on clock interrupt.
  1.1 Table driven
  1.2 Cyclic Scheduler
2. Event-driven Schedulers
  2.1 RMA (Rate Monotonic Analysis)
  2.2 EDF (Earliest Deadline First)
  2.3 DMA (Deadline Monotonic Analysis)
3. Hybrid
  Round-robin

## Slide 3: Earliest Deadline First (EDF)
Dynamic priority scheduling
Whenever a new task arrive, sort the ready queue so that the task closest to the end of its period assigned the highest priority
Preempt the running task if it is not placed in the first of the queue in the last sorting

## Slide 4: Earliest Deadline First (EDF)

## Slide 5: Schedulability Criteria for EDF

## Slide 9: EDF
Exercise 1: Consider the following periodic tasks. Determine whether the task set is schedulable.
T1 = (e1 = 35ms, p1 = 80ms)
T2 = (e2 = 25 ms, p2 = 50ms)

## Slide 10: EDF with period and deadline differ
If deadline is given use the formula for Schedulability Test

## Slide 11: Pros and Cons of EDF
Simple EDF algorithm; it works for all types of tasks: periodic or non periodic
It is simple and works nicely in theory (+)
Simple schedulability test: U <= 1 (+)
Optimal (+)
Best CPU utilization (+)
Difficult to implement in practice. It is not very often adopted due to the dynamic priority-assignment (expensive to sort the ready queue on-line), which has nothing to do with the periods of tasks. Note that Any task could get the highest priority (-)
Non stable: if any task instance fails to meet its deadline, the system is not predictable, any instance of any task may fail (-)

## Slide 12: RMS (Rate Monotonic Scheduling)
a.k.a Rate Monotonic Algorithm (RMA)
Fixed Priority scheduling
  Priority is based on time-period
  Lower the period, higher the priority

## Slide 13: RMA Scheduling

## Slide 14: Schedulability test for RMA
Necessary Condition
  A set of periodic real-time tasks would not be RMA schedulable unless they satisfy the following necessary condition:
Sufficient Condition: Liu and Layland’s condition

## Slide 15: Utilization Bound Test (UB)

## Slide 16: RMA

## Slide 17: Exercise

## Slide 18: RMA

## Slide 20: Why Lehoczky’s Test ?

## Slide 21: Lehoczky’s Criterion for Tasks
NOTE: Correction in fig (b). T1 would execute twice within 150ms. (e2 + 2e1 < p2)

## Slide 22: Lehoczky’s Test
Apply the below formula, when period and deadline are same
Apply the below formula, when period and deadline are different

## Slide 23: RMA Transient Overload Handling
RMA possess good transient overload handling.
Good transient overload condition means that when a lower priority task doesn’t complete within its planned complete time, the higher priority task doesn’t miss the deadline.

## Slide 24: Deadline Monotonic Algorithm (DMA)
RMA no longer remains an optimal scheduling algorithm for the periodic real-time tasks, when task deadlines and periods differ (i.e. d i≠ pi)
DMA is essentially a variant of RMA and assigns priorities to tasks based on their deadlines, rather than assigning priorities

## Slide 25: DMA
Example 1: Is the following task set schedulable by DMA? Also check whether it is schedulable using RMA.
T1 = (e1=10, p1=50, d1=35)
T2 = (e2=15, p2=100, d1=20)
T3 = (e3=20, p3=200, d1=200) [time in msec].
Under DMA, the priority ordering of the tasks is as follows: pr(T2) > pr(T1) > pr(T3).
Checking for T2:
15 msec < 20 msec.
Hence, T2 will meet its first deadline.
Checking for T1:
    (15 + 10) < 35
Hence T1 will meet its first deadline.
Checking for T3:
    (20 + 30 + 40) < 200
Therefore, T3 will meet its deadline.
Therefore, the given task set is schedulable under DMA but not under RMA